## Slide 1: Natural Organic Matter in Water
Formation in Watersheds and Removal in Water Treatment
David A. Reckhow
University of Massachusetts
Notes: 50 min
53 slides

## Slide 2: Exposure to Environmental Contaminants?
You are what you drink

## Slide 3: Exposure to Environmental Contaminants?
You are what you drink?
You are what you shower with?
Or

## Slide 4: Your favorite Water ?
Bottled Water
  $4 per gallon
  $220,000 per year per person
Tap Water
  5c per gallon
  $270 per year per person
150 gpcd

## Slide 5: Outline
Intro & Definitions
NOM Generation
  The Hydrologic Cycle
  Land vs Water sources
  Compounds in NOM
Water Treatment
  Historical
  Types of Treatment
  Components or Processes
Some current issues & popular books
It’s one of my favorite recipes. I call it NOM
5
NOM = Natural Organic Matter

## Slide 6: What’s in the Water?
Natural Substances
  Natural Organic Matter (NOM)
  Inorganic Substances (Iron, Manganese, sodium, chloride)
Anthropogenic Substances
  Pesticides
  Organic Solvents & Other Industrial Compounds
  Carcinogens
  Pharmaceuticals
  Endocrine Disrupting Compounds
  Flame Retardants
Pathogens and other microorganisms

## Slide 7: NOM in Natural Waters: Some definitions
  Groupings Based on Origin
autochthonous compounds are created within the water body
allochthonous compounds can originate from either the soil or from upstream water bodies
aquagenic, substances originating from any water body
pedogenic for substances originating from soil
7

## Slide 8: Watershed Origins
Aquifer
Lake
Upper Soil Horizon
Lower Soil Horizon
Sediment & Gravel in Lake Bed
Litter Layer
Algae
8

## Slide 9: Watershed Origins
Aquifer
Lake
Sediment & Gravel in Lake Bed
Algae
9

## Slide 10: Hydrologic Cycle
Three levels
  Surface runoff, overland flow, direct runoff
  Interflow
  Infiltration, percolation, groundwater flow
D&M, Fig 6-1

## Slide 11
http://www.ec.gc.ca/water/images/nature/grdwtr/a5f2e.htm
During dry periods: base flow

## Slide 12: NOM: Which is the bigger source?
Autochthonous
  Aquatic plants
or
Allochthonous
  land plants

## Slide 13: Aquatic sources: Algae
Scenedesmus quadricauda
Cyclotella sp.
~25% from EOM
pH 7, 20-24ºC, chlorine excess
Algae
From: Plummer & Edzwald, 2001
  [ES&T:35:3661]

## Slide 14: Terrestrial Sources: Leaching Experiments
White
Pine
Red
Maple
White
Oak
Darleen Bryan’s study

## Slide 15: Leaching of leaves
More organic matter released as the leaves remain submerged
Ultraviolet (UV254) absorbance measures a certain fraction
The ratio of UV254 to dissolved organic carbon (DOC) concentration is called SUVA and reflects organic matter reactivity

## Slide 16: Composition of an “average” leaf
250 g/m2/yr EABP
Highly-colored
Some color

## Slide 17: Plant biopolymers
Cellulose
Lignin
  Phenyl-propane units
  Cross-linked
  Radical polymerization
  Ill defined structure
Hemicellulose
Terpeniods
Proteins

## Slide 18: Tannins, Aromatic Acids and Phenols, cont.
Lignin monomers
p-Hydroxybenzoic Acid
Vanillic Acid

## Slide 19: Tannins, Aromatic Acids and Phenols
  About 0.5% of Total
  Plant Products
  Likely THM Precursors
  Source of Color & DBPs
Hydrolyzable Tannin
Condensed Tannin
Gallic Acid monomers
Chemical
Symbols
Notes: Tannins are common plant products found in trees, coffee, cocoa, etc. They all share an ability to turn animal skins into leather, rendering non-putrescable. Some tannins have been used as an antidote to poisons. They have also been useful in the treatment of diarrhea. Some tannins may also play a role in mouth and throat cancer.

## Slide 20: Carbohydrates
empirical formula: Cx(H2O)y
Glucose (monosaccharide) Cellulose (polysaccharide)
Glucosamine (amino sugar)

## Slide 21: Fatty Acids
  maybe 4% of DOC
  other mixed acids may account for 2%
H-COOH CH3-COOH CH3-CH2-COOH
Formic Acid Acetic Acid Propionic Acid
CH3-CH2-CH2-COOH H3-CH2-CH2-CH2-COOH
Butyric Acid Valeric Acid
Common Volatile Fatty Acids in Natural Waters
CH3-COO-
At neutral pH’s most lose H+

## Slide 22: Amino Acids and Proteins
Tyrosine
Simple Amino Acids
  Amine and acid groups
Alanine
Polypeptides & Proteins
  Comprised of many AAs

## Slide 23: NOM Quantification: TOC & DOC
      Oxidation
  High Temperature Pyrolysis
  UV Irradiation
  Heated Persulfate
  UV/Persulfate
Principle: oxidize all organic matter to Carbon dioxide and water. Then measure the amount of carbon dioxide produced
Filter

## Slide 24: Concentrations: Pedogenic
Land Sources
  From Woody & non-woody plants
  Depends on vegetation, soil, hydrology
  Most biodegradable fractions are quickly lost
Attenuated by adsorption to clay soils
  Parallel watersheds in Australia (Cotsaris et al., 1994)
    Clearwater Creek, high clay content: 2.5 mg/L TOC
    Redwater Creek, sandy soil: 31.7 mg/L TOC
Increasing?; link to global warming?
24

## Slide 25: Concentrations: Aquagenic
Algal & aquatic plant Sources
  Depend on nutrient levels / trophic state
Concentrations in Lakes (mg/L) (Thurman, 1985)
Groundwater average: 0.7 mg/L
  No algae, much soil attenuation
25

## Slide 26: John #I: Dr. John Snow
Characterizing “the acute problem”
Cholera
  First emerged in early 1800s
  1852-1860: The third cholera pandemic
    Snow showed the role of water in disease transmission
      London’s Broad Street pump (Broadwick St)
    Miasma theory was discredited, but it took decades to fully put it to rest
1813-1858
2006
Notes: Other books:
The Strange Case of the Broadstreet Pump: John Snow and the Mystery of Cholera (2007)
The Medical Detective: John Snow, Cholera and the Mystery of the Broad Street Pump (2007)
The Blue Death: Disease, Disaster and the Water we Drink (2007)
Cholera, Chloroform and the Science of Medicine: A Life of John Snow (2003)

## Slide 27: Cholera in London & Dr. John Snow
During an outbreak of cholera in London in 1854, John Snow plotted on a map the location of all the cases he learned of. Water in that part of London was pumped from wells located in the various neighborhoods. Snow's map revealed a close association between the density of cholera cases and a single well located on Broad Street.
Removing the pump handle of the Broad Street well put an end to the epidemic. This despite the fact that the infectious agent that causes cholera was not clearly recognized until 1905.
John Snow's map showing cholera deaths in London in 1854 (courtesy of The Geographical Journal). The Broad Street well is marked with an X (within the red circle).
http://www.ph.ucla.edu/epi/snow.html

## Slide 28
Picadilly Circus
Soho, Westminster

## Slide 29: John #2: Dr. John L. Leal
Solutions to “the acute problem”
  Jersey City’s Boonton Reservoir
  Leal experimented with chlorine, its effectiveness and production
    George Johnson & George Fuller worked with Leal and designed the system (1908)
“Full-scale and continuous implementation of disinfection for the first time in Jersey City, NJ ignited a disinfection revolution in the United States that reverberated around the world”
M.J. McGuire, JAWWA 98(3)123
1858-1914
Photo courtesy of the Leal family and Mike McGuire

## Slide 30: Chlorination
Melosi, 2000, The Sanitary City, John Hopkins Press
Greenberg, 1980, Water Chlorination, Env. Impact & Health Eff., Vol 3, pg.3, Ann Arbor Sci.
US Death Rates for Typhoid Fever
1-2 punch of filtration & chlorination

## Slide 31: Today’s Conventional Treatment
Coagulation & solids separation
  Use of alum or another chemical coagulant
  rapid mix, flocculation, settling, filtration
Disinfection
  including clearwell for contact time
Most common sequence for surface water
Dist.
Sys.
Clear
well
Coagulant
Disinfectant
Settling
Corrosion Control
Fluoride
raw water
flocculation
rapid
mix
Filtration
Removes some of the NOM & suspended particles
Kills or inactivates pathogenic organisms

## Slide 32: Coagulation chemistry
Ferric Sulfate
Alum
Mechanisms
Precipitation of metal hydroxide, then:
  Adsorption of contaminants
  Enmeshment of particles

## Slide 33: NOM removal by alum coagulation
Impacts of pH and dose
Mn precipitation
Rennes IV Raw Water
(France) 11/19/84
Reckhow & Bourbigot (unpublished data)

## Slide 34: Flocculation
An Empty full-scale rectangular flocculation tank in Southern CA
MWDSC
Weymouth Plant
12 Dec 05
Can be done in the lab by slowly mixing your sample with a stirrer or on a shaking table

## Slide 35: Settling
Circular and rectangular designs
Can be done in the lab by letting your sample sit in a jar quiescently
MWDSC
Weymouth Plant
12 Dec 05

## Slide 36: Filtration
Sand media
  Empty filter, not in service (Cincinnati)

## Slide 37: Chlorination
Chlorine tanks
  Left side is currently feeding
  Right side is on reserve

## Slide 38: Other Types: Ozone Plants
Many types
  Simplest type: ozone, non-filtration shown below
    examples: MWRA (Boston), Portland ME
  More complex: including coagulation & Filtration
    examples: Andover MA, Amherst MA
  Always includes final disinfection with chlorine or chloramines
Dist.
Sys.
Cl2
Cl2
NH3
O3

## Slide 39: Ozone
Generator
Diffusers
Can be done in the lab with a $70 fish tank sized ozone generator

## Slide 40: Ultraviolet Light
Waterloo, Ont

## Slide 41: Membrane Treatment
National City, CA

## Slide 42: John #III: John Rook
Chlorine: “the chronic problem”
  Brought headspace analysis from the beer industry to drinking water
  Found trihalomethanes (THMs) in finished water
    Carcinogens !?!
  Published in Dutch journal H2O, Aug 19, 1972 issue
  Deduced that they were formed as byproducts of chlorination
  Proposed chemical pathways
Rook, 1974, Water Treat. & Exam., 23:234
1921-2010

## Slide 43: Reactions with Disinfectants: Chlorine
HOCl
+ natural organics
(NOM)
Oxidized NOM
and inorganic chloride
  Aldehydes
Chlorinated Organics
  TOX
  THMs
  HAAs
The THMs
The Precursors!

## Slide 44
a
Hours of transit time
from the water filtration plant
to your house

## Slide 46: Multiple Routes of Exposure
Inhalation in the shower produces highest blood level and response is fast
Gordon et al., 2006 [Env. Health Persp.114:514-521]

## Slide 47: Epidemiology
137,000 at risk in US?
“I think you should be more explicit here
in step two”
Bladder Cancer
  DBPs linked to 9,300 US cases every year
Other Cancers
  Rectal, colon
Reproductive & developmental effects
  Neural tube defects
  Miscarriages & Low birth weight
  Cleft palate
Other
  Kidney & spleen disorders
  Immune system problems, neurotoxic effects
Epidemiology is not supported
by Toxicology of known DBPs

## Slide 48: Observational: The DBP Iceberg
Halogenated Compounds
Non-halogenated Compounds
ICR Compounds
50 MWDSC DBPs
~700 Known DBPs
THMs, THAAs
DHAAs
Stuart Krasner
Susan Richardson

## Slide 49: Another
Sandra Hempel
  Journalist
2007 publication date
Similar in many ways to Johnson’s book

## Slide 50: Biography
A serious biography
  2003 publication
Primarily written by MDs

## Slide 51: Cholera & beyond
Robert Morris
  Environmental epidemiologist
  2007 publication date
More comprehensive
  Cholera to DBPs to Crypto

## Slide 52: Lead Hazards
2006 publication date
Werner Troesken
  Professor of History
Presents many historical lessons on society’s failure to balance public health with profit

## Slide 53: The End
53